## Slide 1
BTEC 2101 · Bioprocess Engineering
Reactors &
Applications in Biochemical Engineering
Bioreactor Types · Growth Kinetics · Sterilization · Scale-Up · Control
B.Tech Biotechnology | 1st Year | Unit 4 Focus

## Slide 2
UNIT 4
Bioreactor Types & Configurations
⚗️ Stirred Tank Reactor (STR)
Most widely used bioreactor in industry
Mechanical agitation ensures homogeneous mixing
Suitable for aerobic & anaerobic fermentations
Operated in batch, fed-batch, or continuous mode
🫧 Airlift & Bubble Column
Pneumatic mixing — no mechanical impeller
Airlift: riser + downcomer for directed flow
Bubble column: simple, low shear for shear-sensitive cells
Used in algae culture, wastewater treatment
🔄 CSTR & Fed-Batch
CSTR: continuous feed + withdrawal at steady state
Dilution rate D = F/V controls growth rate
Fed-batch: extends exponential phase, avoids catabolite repression
Key for antibiotic & recombinant protein production
Slide 2 of 5 · Reactors & Applications in Biochemical Engineering

## Slide 3
UNIT 2
Kinetics of Growth, Substrate Utilization & Product Formation
📐 Reactor Kinetic Equations
Monod Equation:
μ = μmax · [S] / (Ks + [S])
Batch Reactor (no flow):
dX/dt = μ · X
CSTR Balance:
D·(S₀−S) = μ·X / YX/S
Productivity:
P = D · X (CSTR at steady state)
🧬 Reactor Applications
Batch Reactor
Closed system — substrate added at start. Growth follows classic sigmoid curve. Simple but low productivity per unit time.
Fed-Batch Reactor
Substrate fed continuously, no withdrawal. Extends exponential phase. Used for penicillin, baker's yeast, insulin production.
CSTR / Chemostat
Steady-state operation. μ = D (dilution rate). Highest volumetric productivity. Used for SCP and ethanol fermentation.
Plasmid Instability
Recombinant strains can lose plasmids under continuous operation — selection pressure or antibiotic addition needed.
Slide 3 of 5 · Reactors & Applications in Biochemical Engineering

## Slide 4
UNITS 3 & 4
Sterilization · Bioreactor Design · Scale-Up
🌡️ Sterilization for Bioreactors
Thermal death kinetics: N = N₀ · e^(−k·t)
→ k increases with temperature (Arrhenius law)
Del factor (∇): ∇ = ln(N₀/N) — design criterion for sterilisation cycles
In-situ steam sterilization: 121°C, 15 psi — standard for STRs
Continuous sterilization (HTST): less nutrient destruction, preferred at industrial scale
Air sterilization: absolute filters (0.2 μm HEPA) for sparger air supply
All sterilization steps must be validated before reactor inoculation
📐 Scale-Up Strategies
Constant kLa
Maintain oxygen transfer coefficient — most critical for aerobic processes
Constant P/V
Equal power input per unit volume ensures similar mixing intensity
Geometric Similarity
Keep H/D ratios and impeller geometry consistent across scales
Constant Re
Equal Reynolds number preserves fluid flow pattern and turbulence
Slide 4 of 5 · Reactors & Applications in Biochemical Engineering

## Slide 5
UNIT 5 · SUMMARY
Instrumentation, Control & Reactor Applications Summary
🖥 Reactor Instrumentation
Measured variables: pH, DO, temperature, agitation, foam level, CO₂ off-gas
Sensors: pH electrodes, polarographic DO probes, online turbidity meters
PID controllers: auto-regulate temperature, pH and dissolved oxygen setpoints
SCADA / DCS systems: real-time data logging and process visualisation
📚 Course Units at a Glance
Unit | Topic
1 | Microbial Process Principles
2 | Kinetics of Growth & Product Formation
3 | Sterilization Principles
4 | Bioreactor Design & Reactor Applications
5 | Instrumentation & Control
💡 Key Takeaway:
Bioreactors are the core of biochemical engineering — choosing the right reactor type, controlling its environment precisely, and scaling it up reliably determines whether a bioprocess is scientifically sound and industrially viable.
B.Tech Biotechnology — Year 1 · Bioprocess Engineering